## Slide 1: Caches
Module 16 - 24

## Slide 2: How is the Hierarchy Managed?
registers  memory
  By compiler (or assembly level programmer)
cache  main memory
  By the cache controller hardware
main memory  disks (secondary storage)
  By the operating system (virtual memory)
  (Talk about later in the semester)
  Virtual to physical address mapping assisted by the hardware (TLB)
  By the programmer (files)

## Slide 3: Cache Basics: Direct Mapped
Direct mapped
  Each memory block is mapped to exactly one block in the cache
    Many lower level blocks share a given cache block
    Block is also called a line
  Address mapping:
    (block address) modulo (# of blocks in the cache)
    Tag associated with each cache block containing the address information (the upper portion of the address) required to identify the block (to answer Q1)
  (Later in semester we’ll cover alternatives to direct mapped)

## Slide 4: Mapping a 6-bit Memory Address
Note: $ = Cache
In example, block size is 4 bytes/1 word (it could be multi-word)
Memory and cache blocks are the same size, unit of transfer between memory and cache
# Memory blocks >> # Cache blocks
  16 Memory blocks/16 words/64 bytes/6 bits to address all bytes
  4 Cache blocks, 4 bytes (1 word) per block
  4 Memory blocks map to each cache block
Byte within block: low order two bits, ignore! (nothing smaller than a block)
Memory block to cache block, aka index: middle two bits
Which memory block is in a given cache block, aka tag: top two bits
0
5
1
Byte Offset Within Block (e.g., Word)
2
3
Block Within $
Index
4
Mem Block Within $ Block
Tag

## Slide 5: Direct Mapped Cache Example
One word blocks, cache size = 1K words (or 4KB)
20
Tag
10
Index
Data
Index
Tag
Valid
0
1
2
.
.
.
1021
1022
1023
31 30 . . . 13 12 11 . . . 2 1 0
Byte offset
What kind of locality are we taking advantage of?
20
Data
32
Hit
Valid bit ensures something useful in cache for this index
Compare Tag with upper part of Address to see if a Hit
Read data from cache instead of memory if a Hit
Notes: Let’s use a specific example with realistic numbers: assume we have a 1 K word (4Kbyte) direct mapped cache with block size equals to 4 bytes (1 word).
In other words, each block associated with the cache tag will have 4 bytes in it (Row 1).
With Block Size equals to 4 bytes, the 2 least significant bits of the address will be used as byte select within the cache block.
Since the cache size is 1K word, the upper 32 minus 10+2 bits, or 20 bits of the address will be stored as cache tag.
The rest of the (10) address bits in the middle, that is bit 2 through 11, will be used as Cache Index to select the proper cache entry
Temporal!

## Slide 6: Caching: A Simple First Example
00
01
10
11
Cache
0000xx
0001xx
0010xx
0011xx
0100xx
0101xx
0110xx
0111xx
1000xx
1001xx
1010xx
1011xx
1100xx
1101xx
1110xx
1111xx
Main Memory
Tag
Data
Q: Is the mem block in cache?
Compare the cache tag to the high order 2 memory address bits to tell if the memory block is in the cache
Valid
One word blocks
Two low order bits define the byte in the word (32b words)
Q: Where in the cache is the mem block?
Use next 2 low order memory address bits – the index – to determine which cache block (i.e., modulo the number of blocks in the cache)
(block address) modulo (# of blocks in the cache)
Index
Notes: For class handout

## Slide 7: Caching: A Simple First Example
00
01
10
11
Cache
Main Memory
Q: Where in the cache is the mem block?
Use next 2 low order memory address bits – the index – to determine which cache block (i.e., modulo the number of blocks in the cache)
Tag
Data
Q: Is the mem block in cache?
Compare the cache tag to the high order 2 memory address bits to tell if the memory block is in the cache
Valid
0000xx
0001xx
0010xx
0011xx
0100xx
0101xx
0110xx
0111xx
1000xx
1001xx
1010xx
1011xx
1100xx
1101xx
1110xx
1111xx
One word blocks
Two low order bits define the byte in the word (32b words)
(block address) modulo (# of blocks in the cache)
Index
Notes: For lecture
Valid bit indicates whether an entry contains valid information – if the bit is not set, there cannot be a match for this block

## Slide 8: Direct Mapped Cache
Address 0
Consider the main memory word reference string
  0 1 2 3 4 3 4 15
Start with an empty cache - all blocks initially marked as not valid
0000 0001 0010 0011 0100 0011 0100 1111
Notes: For class handout

## Slide 9: Direct Mapped Cache
0
Consider the main memory word reference string
  0 1 2 3 4 3 4 15
00 Mem(0)
miss
Start with an empty 4-word cache - all blocks initially marked as not valid
  1 requests, 1 miss
0000 0001 0010 0011 0100 0011 0100 1111
Notes: For lecture
Reference string is word addresses (or block number since we are using one word blocks) – i.e., the low order two bits used to selected the byte in the 32-bit word are ignored

## Slide 10: Direct Mapped Cache
0
1
2
3
4
3
4
15
Consider the main memory word reference string
  0 1 2 3 4 3 4 15
Start with an empty cache - all blocks initially marked as not valid
Time
Time
00 Mem(0)
miss
00 Mem(0)
Notes: For class handout

## Slide 11: Direct Mapped Cache
0
1
2
3
4
3
4
15
Consider the main memory word reference string
  0 1 2 3 4 3 4 15
00 Mem(0)
00 Mem(0)
00 Mem(1)
00 Mem(0)
00 Mem(0)
00 Mem(1)
00 Mem(2)
miss
miss
miss
miss
miss
miss
hit
hit
00 Mem(0)
00 Mem(1)
00 Mem(2)
00 Mem(3)
01 Mem(4)
00 Mem(1)
00 Mem(2)
00 Mem(3)
01 Mem(4)
00 Mem(1)
00 Mem(2)
00 Mem(3)
01 Mem(4)
00 Mem(1)
00 Mem(2)
00 Mem(3)
01
4
11
15
00 Mem(1)
00 Mem(2)
00 Mem(3)
Start with an empty cache - all blocks initially marked as not valid
  8 requests, 6 misses
0000 0001 0010 0011 0100 0011 0100 1111
Notes: For lecture
Reference string is word addresses (or block number since we are using one word blocks) – i.e., the low order two bits used to selected the byte in the 32-bit word are ignored

## Slide 12: Impacts of Cache Performance
Relative $ penalty increases as processor performance improves (faster clock rate and/or lower CPI)
  Memory speed unlikely to improve as fast as processor cycle time. When calculating CPIstall, cache miss penalty is measured in processor clock cycles needed to handle a miss
  Lower the CPIideal, more pronounced impact of stalls
Processor with a CPIideal of 2, a 100 cycle miss penalty, 36% load/store instr’s, and 2% I$ and 4% D$ miss rates
  Memory-stall cycles = 2% × 100 + 36% × 4% × 100 = 3.44
  So CPIstalls = 2 + 3.44 = 5.44
  More than twice the CPIideal !
What if the CPIideal is reduced to 1?
What if the D$ miss rate went up by 1%?
Notes: For ideal CPI = 1, then CPIstall = 4.44 and the amount of execution time spent on memory stalls would have risen from 3.44/5.44 = 63% to 3.44/4.44 = 77%
For miss penalty of 200, memory stall cycles = 2% 200 + 36% x 4% x 200 = 6.88 so that CPIstall = 8.88
This assumes that hit time (so hit time is 1 cycle) is not a factor in determining cache performance. A larger cache would have a longer access time (if a lower miss rate), meaning either a slower clock cycle or more stages in the pipeline for memory access.

## Slide 13: Multiword Block Direct Mapped Cache
Four words/block, cache size = 1K words
8
Index
Data
Index
Tag
Valid
0
1
2
.
.
.
253
254
255
31 30 . . . 13 12 11 . . . 4 3 2 1 0
Byte offset
20
20
Tag
Hit
Data
32
Block offset
What kind of locality are we taking advantage of?
Notes: to take advantage for spatial locality want a cache block that is larger than word word in size.

## Slide 14: Taking Advantage of Spatial Locality
0
Let cache block hold more than one word
  0 1 2 3 4 3 4 15
1
2
3
4
3
4
15
Start with an empty cache - all blocks initially marked as not valid
0000 0001 0010 0011 0100 0011 0100 1111
Notes: For class handout

## Slide 15: Taking Advantage of Spatial Locality
0
Let cache block hold more than one word
  0 1 2 3 4 3 4 15
1
2
3
4
3
4
15
Start with an empty cache - all blocks initially marked as not valid
00 Mem(1) Mem(0)
miss
0000 0001 0010 0011 0100 0011 0100 1111
Notes: For class handout

## Slide 16: Taking Advantage of Spatial Locality
0
Let cache block hold more than one word
  0 1 2 3 4 3 4 15
1
2
3
4
3
4
15
00 Mem(1) Mem(0)
miss
00 Mem(1) Mem(0)
hit
00 Mem(3) Mem(2)
00 Mem(1) Mem(0)
miss
hit
00 Mem(3) Mem(2)
00 Mem(1) Mem(0)
miss
00 Mem(3) Mem(2)
00 Mem(1) Mem(0)
01
5
4
hit
00 Mem(3) Mem(2)
01 Mem(5) Mem(4)
hit
00 Mem(3) Mem(2)
01 Mem(5) Mem(4)
00 Mem(3) Mem(2)
01 Mem(5) Mem(4)
miss
11
15
14
Start with an empty cache - all blocks initially marked as not valid
  8 requests, 4 misses
Notes: For lecture
Show the 4-bit address mapping – 2-bits of tag, 1-bit of set address (index), 1-bit of word-in-block select

## Slide 17: Miss Rate vs Block Size vs Cache Size
Chart: Block size (bytes)
| 16 | 32 | 64 | 128 | 256
8 KB | 8.5 | 7.5 | 7.25 | 7.75 | 9.5
16 KB | 4 | 2.75 | 2.75 | 3 | 3.5
64 KB | 2 | 1.7 | 1.55 | 1.4 | 1.4
256 KB | 1 | 0.7 | 0.5 | 0.5 | 0.6
Miss rate goes up if the block size becomes a significant fraction of the cache size because the number of blocks that can be held in the same size cache is smaller (increasing capacity misses)
Notes: Increasing the block size usually decreases the miss rate.
A more serious problem is that the miss penalty goes up since it is primarily determined by the time to fetch the block from the next lower level of the hierarchy and load it into the cache.

## Slide 18: Measuring Cache Performance
Assuming cache hit costs are included as part of the normal CPU execution cycle, then
  CPU time = IC × CPI × CC
  = IC × (CPIideal + Memory-stall cycles) × CC
CPIstall
A simple model for Memory-stall cycles
Memory-stall cycles = accesses/program × miss rate × miss penalty
  Will talk about writes and write misses next lecture, where its a little more complicated
Notes: Reasonable write buffer depth (e.g., four or more words) and a memory capable of accepting writes at a rate that significantly exceeds the average write frequency means write buffer stalls are small

## Slide 19: Impacts of Cache Performance
Relative $ penalty increases as processor performance improves (faster clock rate and/or lower CPI)
  Memory speed unlikely to improve as fast as processor cycle time. When calculating CPIstall, cache miss penalty is measured in processor clock cycles needed to handle a miss
  Lower the CPIideal, more pronounced impact of stalls
Processor with a CPIideal of 2, a 100 cycle miss penalty, 36% load/store instr’s, and 2% I$ and 4% D$ miss rates
  Memory-stall cycles = 2% × 100 + 36% × 4% × 100 = 3.44
  So CPIstalls = 2 + 3.44 = 5.44
  More than twice the CPIideal !
What if the CPIideal is reduced to 1?
What if the D$ miss rate went up by 1%?
Notes: For ideal CPI = 1, then CPIstall = 4.44 and the amount of execution time spent on memory stalls would have risen from 3.44/5.44 = 63% to 3.44/4.44 = 77%
For miss penalty of 200, memory stall cycles = 2% 200 + 36% x 4% x 200 = 6.88 so that CPIstall = 8.88
This assumes that hit time (so hit time is 1 cycle) is not a factor in determining cache performance. A larger cache would have a longer access time (if a lower miss rate), meaning either a slower clock cycle or more stages in the pipeline for memory access.

## Slide 20: Average Memory Access Time (AMAT)
Average Memory Access Time (AMAT) is the average to access memory considering both hits and misses
  AMAT = Time for a hit + Miss rate x Miss penalty
What is the AMAT for a processor with a 200 psec clock, a miss penalty of 50 clock cycles, a miss rate of 0.02 misses per instruction and a cache access time of 1 clock cycle?
Potential impact of much larger cache on AMAT?
1 + 0.02 x 50 = 2 clock cycles
Or 2 x 200 = 400 psecs
1) Lower Miss rate
2) Longer Access time (Hit time): smaller is faster
  Increase in hit time will likely add another stage to the pipeline
At some point, increase in hit time for a larger cache may overcome the improvement in hit rate, yielding a decrease in performance
Notes: AMAT = 1 + 0.02x50 = 2

## Slide 21: Handling Cache Misses (Single Word Blocks)
Read misses (I$ and D$)
  Stall execution, fetch the block from the next level in the memory hierarchy, install it in the cache, send requested word to processor, and then let execution resume
Write misses (D$ only)
  Write allocate: Stall execution, fetch the block from next level in the memory hierarchy, install it in cache, write the word from processor to cache, also update memory, then let execution resume
  or
  No-write allocate: skip the cache write and just write the word to memory (but must invalidate cache block since it will now hold stale data)
Notes: Let’s look at our 1KB direct mapped cache again.
Assume we do a 16-bit write to memory location 0x000000 and causes a cache miss in our 1KB direct mapped cache that has 32-byte block select.
After we write the cache tag into the cache and write the 16-bit data into Byte 0 and Byte 1, do we have to read the rest of the block (Byte 2, 3, ... Byte 31) from memory?
If we do read the rest of the block in, it is called write allocate. But the type of access we are going to do is likely to be another write.
So if even if we do read in the data, we may end up overwriting them anyway so it is a common practice to NOT read in the rest of the block on a write miss.
If you don’t bring in the rest of the block, or use the more technical term, Write Not Allocate, you better have some way to tell the processor the rest of the block is no longer valid.

## Slide 22: Cache-Memory Consistency? (1/2)
Need to make sure cache and memory have same value: 2 policies
1) Write-Through Policy: write cache and write through the cache to memory
  Every write eventually gets to memory
  Too slow, so include Write Buffer to allow processor to continue once data in Buffer, Buffer updates memory in parallel to processor

## Slide 23: Cache-Memory Consistency? (2/2)
Need to make sure cache and memory have same value: 2 policies
2) Write-Back Policy: write only to cache and then write cache block back to memory when evict block from cache
  Writes collected in cache, only single write to memory per block
  Include bit to see if wrote to block or not, and then only write back if bit is set
    Called “Dirty” bit (writing makes it “dirty”)

## Slide 24: Sources of Cache Misses (3 C’s)
Compulsory (cold start, first reference):
  1st access to a block, “cold” fact of life, not a lot you can do about it.
    If running billions of instruction, compulsory misses are insignificant
  Solution: increase block size (increases miss penalty; very large blocks could increase miss rate)
Capacity:
  Cache cannot contain all blocks accessed by the program
  Solution: increase cache size (may increase access time)
Conflict (collision):
  Multiple memory locations mapped to the same cache location
  Solution 1: increase cache size (may increase hit time)
  Solution 2: increase associativity (may increase hit time)
Notes: (Capacity miss) That is the cache misses are due to the fact that the cache is simply not large enough to contain all the blocks that are accessed by the program.
The solution to reduce the Capacity miss rate is simple: increase the cache size.
Here is a summary of other types of cache miss we talked about.
First is the Compulsory misses. These are the misses that we cannot avoid. They are caused when we first start the program.
Then we talked about the conflict misses. They are the misses that caused by multiple memory locations being mapped to the same cache location.
There are two solutions to reduce conflict misses. The first one is, once again, increase the cache size. The second one is to increase the associativity.
For example, say using a 2-way set associative cache instead of directed mapped cache.
But keep in mind that cache miss rate is only one part of the equation. You also have to worry about cache access time and miss penalty. Do NOT optimize miss rate alone.
Finally, there is another source of cache miss we will not cover today. Those are referred to as invalidation misses caused by another process, such as IO , update the main memory so you have to flush the cache to avoid inconsistency between memory and cache.
+2 = 43 min. (Y:23)

## Slide 25: Average Memory Access Time (AMAT)
Average Memory Access Time (AMAT) is the average to access memory considering both hits and misses
  AMAT = Time for a hit + Miss rate x Miss penalty
How reduce Miss Penalty?
Notes: AMAT = 1 + 0.02x50 = 2

## Slide 26: Reducing Cache Miss Rates
Use multiple $ levels
With advancing technology, have more room on die for bigger L1 caches and for second level cache – normally a unified L2 cache (i.e., it holds both instructions and data,) and in some cases even a unified L3 cache
E.g., CPIideal of 2, 100 cycle miss penalty (to main memory), 25 cycle miss penalty (to L2$), 36% load/stores, a 2% (4%) L1 I$ (D$) miss rate, add a 0.5% L2$ miss rate
  CPIstalls = 2 + .02×25 + .36×.04×25 + .005×100 + .36×.005×100
  = 3.54 (vs. 5.44 with no L2$)
Notes: Also reduces cache miss penalty

## Slide 27: Local vs. Global Miss Rates
Local miss rate – the fraction of references to one level of a cache that miss
  Local Miss rate L2$ = L2$ Misses / L1$ Misses
Global miss rate – the fraction of references that miss in all levels of a multilevel cache
    L2$ local miss rate >> than the global miss rate
  Global Miss rate = L2$ Misses / Total Accesses
  = L2$ Misses / L1$ Misses x L1$ Misses / Total Accesses
  = Local Miss rate L2$ x Local Miss rate L1$
  AMAT = Time for a hit + Miss rate x Miss penalty
  AMAT = Time for a L1$ hit + (local) Miss rateL1$ x (Time for a L2$ hit + (local) Miss rate L2$ x L2$ Miss penalty)

## Slide 28: Multilevel Cache Design Considerations
Different design considerations for L1$ and L2$
  L1$ focuses on minimizing hit time for shorter clock cycle: Smaller $ with smaller block sizes
  L2$(s) focus on reducing miss rate to reduce penalty of long main memory access times: Larger $ with larger block sizes
Miss penalty of L1$ is significantly reduced by presence of L2$, so can be smaller/faster but with higher miss rate
For the L2$, hit time is less important than miss rate
  L2$ hit time determines L1$’s miss penalty
Notes: Global miss rate – the fraction of references that miss in all levels of a multilevel cache. The global miss rate dictates how often we must access the main memory.
Local miss rate – the fraction of references to one level of a cache that miss

## Slide 29: Improving Cache Performance (1 of 3)
1. Reduce the time to hit in the cache
  Smaller cache
  1 word blocks (no multiplexor/selector to pick word)
2. Reduce the miss rate
  Bigger cache
  Larger blocks (16 to 64 bytes typical)
  (Later in semester: More flexible placement by increasing associativity)

## Slide 30: Improving Cache Performance (2 of 3)
3. Reduce the miss penalty
  Smaller blocks
  Use multiple cache levels
    L2 cache not tied to processor clock rate
  Use a write buffer to hold dirty blocks being replaced so don’t have to wait for the write to complete before reading
  Check write buffer on read miss – may get lucky
  Faster backing store/improved memory bandwidth

## Slide 31: The Cache Design Space (3 of 3)
Several interacting dimensions
  Cache size
  Block size
  Write-through vs. write-back
  Write allocation
  Associativity
  Replacement policy
Optimal choice is a compromise
  Depends on access characteristics
    Workload
    Use (I-cache, D-cache)
  Depends on technology / cost
Simplicity often wins
(Associativity)
Cache Size
Block Size
Bad
Good
Less
More
Factor A
Factor B
Notes: No fancy replacement policy is needed for the direct mapped cache.
As a matter of fact, that is what cause direct mapped trouble to begin with: only one place to go in the cache--causes conflict misses.
No fancy replacement policy is needed for the direct mapped cache.
As a matter of fact, that is what cause direct mapped trouble to begin with: only one place to go in the cache--causes conflict misses.
Besides working at Sun, I also teach people how to fly whenever I have time.
Statistic have shown that if a pilot crashed after an engine failure, he or she is more likely to get killed in a multi-engine light airplane than a single engine airplane.
The joke among us flight instructors is that: sure, when the engine quit in a single engine stops, you have one option: sooner or later, you land. Probably sooner.
But in a multi-engine airplane with one engine stops, you have a lot of options. It is the need to make a decision that kills those people.

## Slide 32: One Word Wide Bus, One Word Blocks
If block size is one word, then for a memory access due to a cache miss, the pipeline will have to stall for the number of cycles required to return one data word from memory
  memory bus clock cycle to send address
  memory bus clock cycles to read DRAM
  memory bus clock cycle to return data
  total clock cycles miss penalty
Number of bytes transferred per clock cycle (bandwidth) for a single miss is
  bytes per memory bus clock cycle
CPU
Cache
DRAM
Memory
bus
on-chip
Notes: For lecture

## Slide 33: One Word Wide Bus, One Word Blocks
If block size is one word, then for a memory access due to a cache miss, the pipeline will have to stall for the number of cycles required to return one data word from memory
  memory bus clock cycle to send address
  memory bus clock cycles to read DRAM
  memory bus clock cycle to return data
  total clock cycles miss penalty
Number of bytes transferred per clock cycle (bandwidth) for a single miss is
  bytes per memory bus clock cycle
CPU
Cache
DRAM
Memory
bus
on-chip
  1
  15
  1
  17
  4/17 = 0.235
Notes: For lecture

## Slide 34: One Word Wide Bus, Four Word Blocks
What if the block size is four words and each word is in a different DRAM row?
  cycle to send 1st address
  cycles to read DRAM
  cycles to return last data word
  total clock cycles miss penalty
Number of bytes transferred per clock cycle (bandwidth) for a single miss is
  bytes per clock
CPU
Cache
DRAM
Memory
bus
on-chip
Notes: For class handout

## Slide 35: One Word Wide Bus, Four Word Blocks
What if block size is four words and each word is in a different DRAM row?
  cycle to send 1st address
  cycles to read DRAM
  cycles to return last data word
  total clock cycles miss penalty
Number of bytes transferred per clock cycle (bandwidth) for a single miss is
  bytes per clock
CPU
Cache
DRAM
Memory
bus
on-chip
15 cycles
15 cycles
15 cycles
15 cycles
1
  4 x 15 = 60
  1
  62
  (4 x 4)/62 = 0.258
Notes: For lecture

## Slide 36: One Word Wide Bus, Four Word Blocks
What if block size is four words and all words are in the same DRAM row?
  cycle to send 1st address
  cycles to read DRAM
  cycles to return last data word
  total clock cycles miss penalty
Number of bytes transferred per clock cycle (bandwidth) for a single miss is
  bytes per clock
CPU
Cache
DRAM
Memory
bus
on-chip
Notes: For class handout

## Slide 37: One Word Wide Bus, Four Word Blocks
What if the block size is four words and all words are in the same DRAM row?
  cycle to send 1st address
  cycles to read DRAM
  cycles to return last data word
  total clock cycles miss penalty
Number of bytes transferred per clock cycle (bandwidth) for a single miss is
  bytes per clock
CPU
Cache
DRAM
Memory
bus
on-chip
15 cycles
5 cycles
5 cycles
5 cycles
1
15 + 3*5 = 30
  1
  32
  (4 x 4)/32 = 0.5
Notes: For lecture

## Slide 38: Interleaved Memory, One Word Wide Bus
For a block size of four words
  cycle to send 1st address
  cycles to read DRAM banks
  cycles to return last data word
  total clock cycles miss penalty
CPU
Cache
DRAM
Memory
bank 1
bus
on-chip
DRAM
Memory
bank 0
DRAM
Memory
bank 2
DRAM
Memory
bank 3
Number of bytes transferred per clock cycle (bandwidth) for a single miss is
  bytes per clock
Notes: For class handout

## Slide 39: Interleaved Memory, One Word Wide Bus
For a block size of four words
  cycle to send 1st address
  cycles to read DRAM banks
  cycles to return last data word
  total clock cycles miss penalty
CPU
Cache
bus
on-chip
Number of bytes transferred per clock cycle (bandwidth) for a single miss is
  bytes per clock
15 cycles
15 cycles
15 cycles
15 cycles
  (4 x 4)/20 = 0.8
1
15
  4*1 = 4
  20
DRAM
Memory
bank 1
DRAM
Memory
bank 0
DRAM
Memory
bank 2
DRAM
Memory
bank 3
Notes: For lecture
The width of the bus and the cache need not be changed, but sending an address to several banks permits them all to read simultaneously. Interleaving retains the advantage of incurring the full memory latency only once.
Low order interleaving (low order bits select bank, high order bits used to access DRAM banks in parallel).
Low order memory interleaving, i.e.,
Bank 0 holds addresses xx…xx00
Bank 1 holds addresses xx…xx01
Bank 2 holds addresses xx…xx10
Bank 3 holds addresses xx…xx11
May want to add another example where you also have a wide bus (e.g., a 2 word bus between the interleaved memory and the processor).

## Slide 40: Performance Programming: Adjust software accesses to improve miss rate
Now that understand how caches work, can revise program to improve cache utilization
  Cache size
  Block size
  Multiple levels

## Slide 41: Performance of Loops and Arrays
Array performance often limited by memory speed
OK if access memory different order as long as get correct result
Goal: Increase performance by minimizing traffic from cache to memory
  That is, reduce Miss rate by getting better reuse of data already in cache
One approach called Cache Blocking: “shrink” problem by performing multiple iterations within smaller cache blocks
Notes: PICTURE HEAT FLOW
Cache-blocking algorithms “shrink” problem by PERFORMING MULTIPLE ITERATIONS WITHIN SMALLER CACHE BLOCKS
There are many factors that impact cache performance. Effective use of data cache locality is one such significant factor. And the well known data cache blocking technique is used to take advantage of data cache locality. The cache blocking technique restructures loops with frequent iterations over large data arrays by sub-dividing the large array into smaller blocks, or tiles. Each data element in the array is reused within the data block, such that the block of data fits within the data cache, before operating on the next block or tile. Depending on the application, a cache data blocking technique is very effective. It is widely used in linear algebra and is a common transformation applied by compilers and application programmers. Since the 2nd level unified cache contains instructions as well as data, compilers often try to take advantage of instruction locality by grouping related blocks of instructions close together as well. Typical applications benefiting from cache data blocking are image or video applications where the image can be processed on smaller portions of the total image or video frame. But the effectiveness of the technique is highly dependent on the data block size, the processor's cache size, and the number of times the data is reused. At the sweet spot around 450-460 KB tiles size matches very closely with unified L2 cache size, the application almost doubles in performance. This is only an example and the block size sweet spot for any given application will vary based on how much of the L2 cache is used by other cached data within the application as well as cached instructions from the application. Typically, an application should target the block size to be approximately one-half to three-quarters of the cache size. In general, it's better to err on the side of having too small of a block size than too large. Additionally, the data cache blocking technique performance scales well with multiple processors if the algorithm is threaded for data decomposition. Fortunately, the fact that each block of data can be processed independently with respect to other blocks lends itself to being decomposed into separate blocks which can be processed in separate threads of execution. Figure 2.0 also shows the performance improvement of the cache blocking algorithm for two threads running on a dual processor system with two physical processors. The performance curve for two threads matches v ery closely the performance curve for a single processor system with the sweet spot for the block size at around 450-460 KB per thread but at approximately twice the performance. Assuming there is very little synchronization necessary between the two threads as in this example, it's reasonable to expect that the block size sweet spot would not vary significantly. Both processors have independent cache of equal size. In this case, both processors have 512KB of L2 cache available.

## Slide 42: Loop Interchange
/* Before */
For (j = 0; j <10; j = j+1)
for (i = 0; i < 5000;p i = i+1)
x[i][j] = 2 * x[i][j]
/* After*/
For (i = 0; i <5000; i = i+1)
for (j = 0; j< 10; j = j+1)
x[i][j] = 2 * x[i][j]
Loop reordering maximizes
The use of data in a cache
block before it is discarded

## Slide 43: Matrix Multiplication
*
=
c
a
b

## Slide 44: Matrix Multiplication
c
=
*
a
b
ai*
b*j
cij
Simple Matrix Multiply - www.youtube.com/watch?v=yl0LTcDIhxc
100 x 100 Matrix, Cache 1000 blocks, 1 word/block

## Slide 45: The simplest algorithm
for (i=0;i<N;i++)
for (j=0;j<N;j++)
for (k=0;k<N;k++) c[i][j] += a[i][k] * b[k][j];
Assumption: the matrices are stored as 2-D NxN arrays
Advantage: code simplicity
Disadvantage: Marches through memory and caches

## Slide 46: Note on Matrix in Memory
A matrix is a 2-D array of elements, but memory addresses are “1-D”
Conventions for matrix layout
  by column, or “column major” (Fortran default); A(i,j) at A+i+j*n
  by row, or “row major” (C default) A(i,j) at A+i*n+j
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
0
4
8
12
16
1
5
9
13
17
2
6
10
14
18
3
7
11
15
19
Column major
Row major
Cache blocks
Blue row of matrix is stored in red cache blocks
Column major matrix in memory

## Slide 47: Improving reuse via Blocking: 1st “Naïve” Matrix Multiply
{implements C = C + A*B}
for i = 1 to n
{read row i of A into cache}
for j = 1 to n
{read c(i,j) into cache}
{read column j of B into cache}
for k = 1 to n
c(i,j) = c(i,j) + a(i,k) * b(k,j)
{write c(i,j) back to main memory}
=
+
*
C(i,j)
A(i,:)
B(:,j)
C(i,j)

## Slide 48: Linear Algebra to the Rescue!
Instead of Multiplying two, say, 6 x 6 matrices
Thus, can get same result as multiplication of a set of submatricies

## Slide 49: Blocked Matrix Multiply
Consider A,B,C to be N-by-N matrices of b-by-b subblocks where b=n / N is called the block size
for i = 1 to N
for j = 1 to N
{read block C(i,j) into cache}
for k = 1 to N
{read block A(i,k) into cache}
{read block B(k,j) into cache}
C(i,j) = C(i,j) + A(i,k) * B(k,j) {do a matrix multiply on blocks}
{write block C(i,j) back to main memory}
=
+
*
C(i,j)
A(i,k)
B(k,j)
C(i,j)
Blocked Matrix Multiply - www.youtube.com/watch?v=IFWgwGMMrh0
100 x 100 Matrix, 1000 cache blocks, 1 word/block, block 30x30

## Slide 50: Another View of “Blocked” Matrix Multiplication
C11
C22 = A21B12 + A22B22 + A23B32 + A24B42 =
k A2k*Bk2
Main Point: each multiplication operates on small “block” matrices, whose size may be chosen so that they fit in the cache.
C12
C13
C14
C21
C22
C23
C24
C31
C32
C43
C34
C41
C42
C43
C44
A11
A12
A13
A14
A21
A22
A23
A24
A31
A32
A33
A34
A41
A42
A43
A144
B11
B12
B13
B14
B21
B22
B23
B24
B32
B32
B33
B34
B41
B42
B43
B44
N = 4 *r

## Slide 51: Blocked Algorithm
The blocked version of the i-j-k algorithm is written simply as (A,B,C are submatricies of a, b, c)
for (i=0;i<N/r;i++)
for (j=0;j<N/r;j++)
for (k=0;k<N/r;k++)
C[i][j] += A[i][k]*B[k][j]
  r = block (sub-matrix) size (Assume r divides N)
  X[i][j] = a sub-matrix of X, defined by block row i and block column j
r x r matrix multiplication
r x r matrix addition

## Slide 52: Maximum Block Size
The blocking optimization works only if the blocks fit in cache.
That is, 3 blocks of size r x r must fit in memory (for A, B, and C)
M = size of cache (in elements/words)
We must have: 3r2  M, or r  √(M/3)
Ratio of cache misses blocked vs. unblocked up to ≈ √M
Simple Matrix Multiply Whole Thing - www.youtube.com/watch?v=f3-z6t_xIyw
Blocked Matrix Multiply Whole Thing - www.youtube.com/watch?v=tgpmXX3xOrk
1x1 blocks: 1,020,000 misses: read A once, read B 100 times, read C once
30x30 blocks: 90,000 misses = read A and B four times, read C once
“Only” 11X vs 30X Matrix small enough that row of A in simple version fits completely in cache; other things