## Slide 1: Computer Architecture Part 1 The Concepts Module 5 - 15
Notes: v10: 28/04/03, Chris Shore
slide 4: added China to text (already on graphic). Updated employee count and geographical distribution.
slide 19: added V6
slides 32: Imported from RV Overview to replace original ADS slide.
slide 33: New general debug architecture diagram
slide 34: new product montage (crib in notes)
slide 35: New question about embedded trace.
v09: 19/11/02, Chris Shore
slides 6-8: New slides showing IP deployment (imported from 926 core module)
v08: 08/02, Rob Levy
- Style update, black & white view amended
v07: 12/01, CJS
Main changes:
- ARM Development Boards slide removed (now in Debug Solutions module)
- Register set slides re-ordered so that the animated graphic comes first
- slide 12: Q bit in v5TEJ as well as v5TE
- slide 14: CPSR changes rephrased slightly
- slide 16: reference to v5T removed.
- slide 27: EASY/Micropack replaced with ADK/ACT
- slide 30: Trace slide updated

## Slide 2: Computing Environment
Computer Architecture
Compiler Techniques
Operating system
&
Software Techniques
Implementation
Instruction Set Architecture
Loop Transformation &
Procedure inlining
Register Allocation
Local and Global Optimization &
Pipeline Scheduling

## Slide 3: The basics…
Non-pipelined processor.
Assume that each operation
takes 75ns
Pipelined processor with 5 stages
Assume each stage takes 17ns.
1st Output 75ns
2nd Output 150ns
3rd Output 225ns
… … ….
1st Output 85ns
2nd Output 102ns
3rd Output 119ns
F
F
D
E
M
W
Pipe-lining is a good idea as long as we manage to keep it filled…
Processor A
Processor B
Proc A Speed = 13.33MHz
Proc. B Speed = 58.82MHz

## Slide 4: Outline
Issues in Pipelining (understanding the rules of the game!)
  Data Dependency / Hazard
  Structural Dependency / Hazard
  Control Dependency / Hazard
ILP, LLP
Branch Prediction and Speculation
Complex pipelining
Superscalar or VLIW?
  In order and out of order (issue, execution and retirement)

## Slide 5: Single issue pipeline architecture
In such single issue pipeline, the upper limit of performance is 1 clock cycle per instruction (CPI)
Many road blocks in achieving the CPI = 1
  Data Flow related issues
  Limitation of resources
  Branches
Instruction
Fetch
Shift + ALU
Memory
Access
Reg
Write
Reg
Read
Reg
Decode
FETCH
DECODE
EXECUTE
MEMORY
WRITE

## Slide 6: Data Dependencies…
Dependences are the property of a program (Data flow)
Date Dependence conveys
  Order in which results must be calculated
  Potential for a hazard, but actual hazard and length of any stall is a property of the pipeline
I: ADD R1,R2,R3
J: SUB R4,R1,R3
  Upper bound on exploitable instruction level parallelism
Dependencies that flow through memory locations are difficult to detect eg [R1, #32] and [R4, #8] might be pointing to the same memory location

## Slide 7: Data Hazard
RAW Hazard (Read after Write) – Due to Data Dependency
Instruction J tries to read operand before Instr. I writes it I: ADD R1,R2,R3
J: SUB R4,R1,R3
Caused by a “Dependence” (in compiler nomenclature).
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Time (clock cycles)
I: add r1,r2,r3
J: sub r4,r1,r3
Value of R1 generated
Value of R1 needed

## Slide 8: Solutions
Reg
ALU
DMem
Ifetch
Reg
Reg
Ifetch
ALU
DMem
Reg
Bubble
Bubble
Wait till the Value of R1
Becomes available
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Do Data Forwarding

## Slide 9
Data forwarding can not solve all the problems (Load interlock)
Solution: Wait and your problems will go away!
Reg
Ifetch
ALU
DMem
Reg
Bubble
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
LDR R1, [R2]
SUB R4,R1,R6
LDR R1, [R2]
SUB R4,R1,R6
Time (clock cycles)

## Slide 10: Data Hazard (continued)
WAR Hazard (Write after Read) – Due to Anti-dependence
Instr I writes operand before Instr J reads it
No problem of WAR hazard in simple “in-line” pipelining
Will cause a problem in multiple issue, out of order execution
I: SUB R4,R1,R3
J: add R1,R2,R3

## Slide 11
WAW hazard (Write after Write) – Due to Output dependence
Instr J writes operand before Instr I writes it
No possibility of WAW hazard in simple “in-line” pipelining
Will become an issue when out of order execution is allowed
I: SUB R1,R4,R3
J: ADD R1,R2,R3

## Slide 12: Name Dependence
Two instructions use the same name but no flow of information
Not a true data dependence, but is a problem when reordering instructions
  Antidependence: instruction j writes a register or memory location that instruction i reads
    Initial ordering (i before j) must be preserved
  Output dependence: instruction i and instruction j write the same register or memory location
    Ordering must be preserved
To resolve, use register renaming technique

## Slide 13: Structural hazard
Hardware can not support the given combination of instructions. If there is just one memory system for instruction and data then structural hazard may occur.
For complex pipeline with split execution unit (many functional units) structural hazard may occur.
Solution? Wait….

## Slide 14: Control Hazard
Ordering of an instruction i with respect to a branch instruction
  Instruction control dependent on a branch cannot be moved before the branch so that its execution is no longer controlled by the branch
  An instruction not control dependent on a branch cannot be moved after the branch so that its execution is controlled by the branch
  If some how we can predict the behavior of branch or even better - eliminate them, then code execution would be very fast.

## Slide 15: Final word on dependences
Preserving Control dependence is a simple and effective way of maintaining program correctness
However, Control dependence is not a fundamental performance limit
Control dependence can be violated if;
  Exception behavior &
  Data Flow
are maintained
Preserving the Exception behavior means that any change in the order of the instruction execution should not change how exception are raised in the program

## Slide 16: So what happens to the pipeline CPI?
Pipeline CPI = Ideal CPI + structural stalls + RAW stalls +
WAR stalls + WAW stalls + Control stalls
What can we do about these stall penalties?

## Slide 17: Overview of Techniques used for reducing stalls
Technique | Target
ISA based techniques | Control hazard stalls
Forwarding and Bypassing | Potential data hazard stalls
Delayed Branches | Control hazard stalls
Dynamic Scheduling | Data hazard stalls from true dependence
Dynamic Scheduling with renaming | Data hazard stalls & name dependencies stalls
Dynamic Branch Prediction | Control hazard stalls
Multiple Instruction per cycle | Ideal CPI
Speculation | Data hazard and Control hazard stalls
Loop Unrolling | Control hazard stalls
Compiler dependence analysis | Ideal CPI, Data hazard stalls
Software pipelining, trace scheduling | Ideal CPI, Data hazard stalls

## Slide 18: ISA based solution…
A cleaver solution has been created to address some of the control stalls
In ARM instruction set, almost every instruction may be conditionally executed.
There are 16 possible condition starting from “Always” to “Never” (which is not used. Code reserved for future expansion).
(conventional way) (ARM way)
  CMP R3,#0 CMP R3,#0
  BEQ SKIP ADDNE R0,R1,R2 ADD R0,R1,R2
  Skip
The conventional way could waste up to three cycles!

## Slide 19: Another example…
Take a look at following C
code
int gcd (int i, int j)
{
while (i != 0)
{
if (i > j)
i -= j;
else
j -= i;
}
return i;
}
Equivalent ARM assembly language code would be
Loop CMP Ri, 0 ; set condition
; “NE” if (i != 0)
; “GT” if (i > j)
; “LT” if (i < j)
SUBGT Ri, Ri, Rj ; if GT, i = i – j
SUBLT Ri, Rj, Ri ; if LT, j = j – i
BNE Loop
This code avoids branches around “then” and “else” clause.

## Slide 20: Branch Prediction
If branches can be predicted (Taken or Not-Taken) with high percentage, then we can reduce stalls by fetching the “target instruction” earlier
When is information about branches gathered/applied?
– When the program is compiled (“compile-time” or Static)
– As the program is being executed (“dynamic”)
– When a “training run” of the program is executed
(“profile-based”) … compile – profile - compile
Prediction is a gamble!
Performance gain = ƒ(accuracy, cost of misprediction)

## Slide 21: Static Branch Prediction Techniques
Static Branch prediction.
Simple to implement. Not much hardware required.
Can be used as a fall through mechanism.
  Predict always not taken
  Predict always taken
  Backward branch predict taken, forward
  branch predict not taken.

## Slide 22: Dynamic Branch Prediction
Dynamic Branch Prediction Scheme.
  Learning based on the past behavior.
Temporal correlation
  The way a branch resolves may be a good predictor of the way it will resolve at the next execution
Spatial correlation
  Several branches may resolve in a highly correlated manner (a preferred path of execution)

## Slide 23: Dynamic Branch Prediction Schemes
1-bit Branch-Prediction Buffer
2-bit Branch-Prediction Buffer
Correlating Branch Prediction Buffer
Tournament Branch Predictor
Branch Target Buffer
Integrated Instruction Fetch Units
Return Address Predictors

## Slide 24: Dynamic Branch Prediction (Contd.)
Take advantage of the knowledge of temporal correlation.
Use Branch prediction buffer
Example; Consider 1 bit prediction buffer; 0 = branch not taken and 1 = branch taken
Suppose we have to take this loop 100 times, how will one bit branch prediction scheme perform?
loop | CMP | Ri, 0 | ; Set Condition ; “NE” if (i != 0) ; “GT” if (i > j) ; “LT” if (i < j)
 | SUBGT | Ri, Ri, Rj | ; if GT, i = i - j
 | SUBLT | Ri, Rj, Ri | ; if LT, j = j – i
 | BNE | loop | 

## Slide 25: One Bit Branch Prediction Counter
Branch History Table (BHT): Lower bits of PC address index table of 1-bit values
  Says whether or not branch taken last time ( T-Taken, NT Not taken )
  No full address check (saves HW, but may be wrong)
In a given single loop, One bit branch prediction counter will provide two wrong predictions;
  First time through the loop, when it predicts exit instead of looping
  Last time through the loop, when it predicts looping instead of exit
How about using a two bit counter?

## Slide 26: Dynamic Branch Prediction (2 bit counter)
Can we better the performance ?
Use two bit branch prediction buffer… i.e. change prediction only when the prediction is wrong twice.
T
T
NT
NT
Predict Taken
Predict Not
Taken
Predict Taken
Predict Not
Taken
T
NT
T
NT
11
10
00
01

## Slide 27: Can we do better with n-bit counter?
n-bit predictor:
  counter can hold values between 0 and
  predict taken when value is greater than or equal to half of maximum value:
  The counter is incremented on each taken branch
  and decremented on each not taken branch
Not much benefit over 2 bit counter…

## Slide 28: Dynamic Branch Prediction (Contd.)
How about Spatial correlation?
Consider following example…
If first condition fails, second condition also fails
Global History Buffer (GHB), records the direction of the last N branches executed by the processor
if (x[i] < 7) then
y += 1;
if (x[i] < 5) then
c -= 4;

## Slide 29: Correlating Branch predictor
Hypothesis: Previous 2-bit predictor schemes use only the recent behavior of a single branch to predict the future behavior of that branch
But branches are correlated; that is, behavior of recently-executed branches affects prediction of current branch
if (aa == 2)
aa = 0; #Branch 1
if (bb == 2)
bb = 0; #Branch 2
if (aa! = bb) { #Branch 3
Clearly branch #3 depends on outcome of #1 and #2
Prediction must be a function of own branch as well as recent outcomes of other branches

## Slide 30: Correlating Branch predictor (cont.)
Idea: record m most recently executed branches as taken or not taken, and use that pattern to select the proper n-bit branch history table
In general, (m,n) predictor means record last m branches to select between 2m history tables, each with n-bit counters
  Thus, old 2-bit BHT is a (0,2) predictor
Global Branch History: m-bit shift register keeping T/NT status of last m branches
Each entry in table has m n-bit predictors

## Slide 31: Correlating Branches
(2,2) predictor
Behavior of recent branches(global branch history) is used to select between four predictions of next branch, updating just that prediction
Branch address(low-order bits)
2-bits per branch predictor
Prediction
2-bit global branch history
4 bits
NN
NT
TN
TT
N
T
SHIFT

## Slide 32: Tournament Predictors
Tournament Predictors are the most popular form of Multilevel branch predictors
Use 2-bit saturating counter per branch to choose between two different predictors
Use choice predictor to choose between global and local predictors
n/m means:
n = left predictor value
m = right predictor value
0: Incorrect
1: Correct
Notes: gdhgfdgf

## Slide 33: Branch Target Predictions
We have been looking at the ways to predict direction of branches (Taken/Not-Taken)
It would be beneficial if we could predict the branch address (target address) and fetch it ASAP
– Branch Target Buffer (BTB)
• Branch target buffer (BTB) stores address of the last target location to avoid recomputing
    Useful for conditional/unconditional branches
– Return Address Stack (RAS)
• Useful for procedure returns

## Slide 34: Branch Target Buffer
Global history buffer Only predicts branch direction. Therefore, cannot redirect fetch stream until after branch target is determined. This is no good.
Use Branch Target Buffer along with GHB.
BTB stores PCs the same way as caches
The PC of a branch is sent to the BTB
When a match is found the corresponding Predicted PC is returned
If the branch was predicted taken, instruction fetch continues at the returned predicted PC
Zero cycle unconditional branch and some times zero cycle conditional branch (Branch folding)

## Slide 35: BTB flow chart
Taken
Branch?
Entry found in branch-target buffer?
Send out predicted PC
Is instruction a taken branch?
Send PC to memory and branch-target buffer
Enter branch instruction address and next PC into branch-target buffer
Mispredicted branch, kill fetched instruction; restart fetch at other target; delete entry from target buffer
Normal instruction execution
Branch correctly predicted; continue execution with no stalls
No
Yes
Yes
Yes
No
No
ID
IF
EX

## Slide 36: BTB with GHB
Yes: instruction is branch and use predicted PC as next PC
No: branch not
predicted, proceed normally
(Next PC = PC+4)
Branch PC
Predicted PC
=?
PC of instruction
FETCH
Extra
prediction state
bits

## Slide 37: Price to pay for Misprediction
In a simple “in order” architecture, kill all instructions behind the mispredicted branch.
Fetch from the new PC value.
How about interrupts?

## Slide 38: Return Address Predictors
Procedure returns account for ~85% of indirect jumps (jumps whose address varies at run time). It will then return to many different locations—BTB may not predict accurately,
Therefore, small buffer of Return Addresses=cache of the most recent return addresses
• Like a hardware stack, LIFO
– At Procedure Call => Push Return address onto stack
– Procedure Return => Prediction off of top of stack, Pop it
• RAS tends to work quite well since call depths are typically not large