## Slide 1: ILP vs Reducing Cache misses
Sometimes a compiler has to choose between improving ILP and improving cache performance
Example:
for (i= 0; i < 512; i = i + 1)
for (j = 1; j < 512; j = j + 1)
x[i][j] = 2*x[i][j-1];
This code accesses the data in the order they are stored thus minimizing the cache misses, but if you unroll the loop, you will find that
for (i= 0; i < 512; i = i + 1)
for (j = 1; j < 512; j = j + 4) {
x[i][j] = 2*x[i][j-1];
x[i][j+1] = 2*x[i][j];
x[i][j+2] = 2*x[i][j+1];
x[i][j+3] = 2*x[i][j+2];
};
Here last three statements have RAW dependency…

## Slide 2
To improve the parallelism, two loops can be interchanged…
for (j = 1; j < 512; j = j + 1)
for (i= 0; i < 512; i = i + 1)
x[i][j] = 2*x[i][j-1];
Unrolling this loop would show
for (j = 1; j < 512; j = j + 1)
for (i= 0; i < 512; i = i + 4){
x[i][j] = 2*x[i][j-1];
x[i+1][j] = 2*x[i+1][j-1];
x[i+2][j] = 2*x[i+2][j-1];
x[i+3][j] = 2*x[i+3][j-1];
};
Now all four statements are independent and can be executed in parallel
But this would lead to memory accesses that would hop through memory thus reducing spatial locality and cache hit rate…