## Slide 1: Multi Core Processors Module 25-27
Notes: v10: 28/04/03, Chris Shore
slide 4: added China to text (already on graphic). Updated employee count and geographical distribution.
slide 19: added V6
slides 32: Imported from RV Overview to replace original ADS slide.
slide 33: New general debug architecture diagram
slide 34: new product montage (crib in notes)
slide 35: New question about embedded trace.
v09: 19/11/02, Chris Shore
slides 6-8: New slides showing IP deployment (imported from 926 core module)
v08: 08/02, Rob Levy
- Style update, black & white view amended
v07: 12/01, CJS
Main changes:
- ARM Development Boards slide removed (now in Debug Solutions module)
- Register set slides re-ordered so that the animated graphic comes first
- slide 12: Q bit in v5TEJ as well as v5TE
- slide 14: CPSR changes rephrased slightly
- slide 16: reference to v5T removed.
- slide 27: EASY/Micropack replaced with ADK/ACT
- slide 30: Trace slide updated

## Slide 2: Tricks we explored till now
ILP
LLP
Branch Prediction
Trace scheduling
Superscalar
VLIW
Out of Order

## Slide 3: Where do we stand…
1990s to 2005 was the era of ILP to achieve maximum performance

## Slide 4: The Limiting Factors
The Power Wall
P = α CLV2ddf + VddIst + VddIleak
If we increase frequency, power will go up.
Compensate it by lowering the Vdd
Unfortunately increases the delay of the logic elements
So have more pipeline stages
But Increasing the pipeline stages may increase CPI due to branches and other hazards.
With shrinking device sizes, power density is the major concern!

## Slide 5: Power Wall…

## Slide 6: Limiting Factors…
ILP wall
Limit studies Cap CPI at 0.01 to 0.0025. Realistically, current processors are tied to CPI of 1 to 0.5
-- Clock rate: at the wall each increase in clock rate has a
corresponding CPI increase (branches, other hazards)
– Instruction fetch and decode: at the wall more
instructions cannot be fetched and decoded per clock
cycle
– Cache hit rate: poor locality can limit ILP and it adversely
affects memory bandwidth

## Slide 7: Limiting Factors…
Memory Wall
Modern Processors take up to 200 cycles to access DRAM!

## Slide 8: Limiting factors…
On die caches are both area intensive and power intensive
StrongArm dissipates more than 43% power in Caches
Huge area cost also included
Larger Caches never deliver the performance boost that frequency ramping provides.

## Slide 9: And so..
Power Wall + ILP Wall + Memory Wall = Brick Wall!!!

## Slide 10: The Solution
In place of a single complex core, can we have several simple cores on a chip? It can solve the power wall problem…
Can we divide up the work between processors in such a way that it can be performed independently and in parallel? This means that the individual core may run at a slower freq and still give a combined higher performance when compared to a uni-processor.
Can we divide each task into several threads which can run in a pseudo-parallel fashion on a single processor or in a true sense on a real multi-processor system.
Are we talking about threads and thread level parallelism (TLP)?

## Slide 11: What is a thread
Threads are defined as light-weight processes
It is a way for a program to fork it self in to two or more simultaneously or pseudo-simultaneously running tasks.
How are threads different from processes
  A Process has to have resource like memory, file handles, sockets, device handles and windows.
  Processes do not share address spaces except through explicit methods .
  At least one thread exists in each process (definition)
  If there are multiple threads then they share all the resources.

## Slide 12: Multi-threading on a single processor
The idea is at least two decades old.
Operating systems like Unix, Linux have been using multi-tasking since long. Gives illusion of parallel execution.
Extend the idea to an individual process that can do more than one thing (say thread) at a time.
User level threads (some times referred to as fibers) and kernel level threads.

## Slide 13: Note of caution to all future “threaders”
Consider following code fragment; assume that function is being called from two threads, A and B.
int i; /* global variable */
………………………..
Void fn(void)
{
for (i = 0; i != 4; i++) {
printf ( “%d “, i);
}
Printf(“\n”);
}
………………………….
What is the expected output?
0 1 0 1 2 2 3 3
What if the answer is
0 1 0 1 2 3 4 5 6 7 8 9 …
What could be the reason???

## Slide 14: Lessons Learnt
Do not use global data (as much as possible)
If i was declared local to fn() then each thread would have it’s own copy.
What if it is necessary to use global data (shared data)?
Use Mutual exclusion…
int i; /* global variable */
pthread_mutex_t loopLock = PTHREAD_MUTEX_INITIALIZER;
void fn( void )
{
pthread_mutex_lock( &loopLock );
for( i = 0; i != 4; ++i ) {
printf( "%d ", i );
}
printf( "\n" );
pthread_mutex_unlock( &loopLock ); } . .
Output = 0 1 2 3
0 1 2 3

## Slide 15: Why use Multithreading on a single Processor?
Each thread runs until it blocks, explicitly relinquishes its control, or the scheduler decides that another thread should get a turn.
A thread may block when it is waiting for some time consuming operation. (generally I/O op)
Scheduler then tells another waiting thread to run.
Time-slicing also possible.

## Slide 16: Multicore
We have already made a case for using Multi-core architecture.
Threads can run in truly parallel fashion when more than one processors are present.
Intel dual core

## Slide 17: IBM Cell processor

## Slide 18: High performance and Embedded computing
Lots of similarities between top of the line high performance computing and Embedded computing.
Both are concerned with power
Efficient Hardware utilization
Software written from scratch so hand tuning possible
What is the difference?
Embedded systems are traditionally concerned with real time computing where as High performance systems have to be blazingly fast.

## Slide 19: Some ground rules for multi-core…
“A parallel computer is a collection of processing elements that cooperate and communicate to solve large problems fast.”
Parallel Architecture = Computer Architecture + Communication Architecture
2 classes of multi-processors WRT memory:
  Centralized Memory Multiprocessor
  < few dozen processors
  Small enough to share single, centralized memory
  Physically Distributed-Memory multiprocessor
  Larger number chips and cores than CMM.
  BW demands  Memory distributed among processors

## Slide 20: Centralized Vs. Shared Memory Arch.
P
1
C
Inter
connection network
C
P
n
M
M
P
1
C
Inter
connection network
C
P
n
M
M
Centralized Memory
Shared Memory

## Slide 21: Centralized Memory Processor
  Also called symmetric multiprocessors (SMPs) because single main memory has a symmetric relationship to all processors
  Large caches  single memory can satisfy memory demands of small number of processors
  Can scale to a few dozen processors by using a switch and by using many memory banks
  Although scaling beyond that is technically conceivable, it becomes less attractive as the number of processors sharing centralized memory increases

## Slide 22: Distributed Memory processor
  Pro: Cost-effective way to scale memory bandwidth
    If most accesses are to local memory
  Pro: Reduces latency of local memory accesses
  Con: Communicating data between processors more complex
  Con: Must change software to take advantage of increased memory BW

## Slide 23: Communication is the Key
Communication occurs by explicitly passing messages among the processors: message-passing multiprocessors
Communication occurs through a shared address space (via loads and stores): shared memory multiprocessors either
  UMA (Uniform Memory Access time) for shared address, centralized memory MP
  NUMA (Non Uniform Memory Access time multiprocessor) for shared address, distributed memory MP

## Slide 24: Symmetric Shared Memory Architecture
Caching shared data by several processors in their individual caches causes a problem.
Some “Cache coherence” mechanism is required.
Basic schemes (protocols) for enforcing coherence are
  Snooping
  Directory based

## Slide 25: What is Memory Coherence
Preserve Program order: Assume a read by Processor P on location X, followed by a write by the same processor P on location X. If no other processor has updated location X between the read and write by P, then location X would always return the value written by P.
Coherent View of Memory: A read by a Processor P1 to location X that follows a write by another processor P2, returns the value updated by P2 if the write and read are sufficiently spread apart
Write serialization: All processors see the same order of
writes to a variable

## Slide 26: Coherency vs. Consistency
Consistency (multi-processor context):
  The issue of exactly when a written value is seen by a “reader” is defined by a memory consistency model
Coherency Vs. Consistency:
  Consistency is concerned with updates/invalidations to a
single shared variable
  Coherency is concerned with the behavior of memory
references from multiple concurrent threads
Notes: Cache coherency and consistency define the action of the processors to maintain coherence. More precisely, coherency defines what value is returned on a read, and consistency defines when it is available
Multiprocessor Consistency
• When does a memory write show up at another CPU?
• A programming model
u Multiprocessor Coherence
• How are memory accesses coordinated among CPUs?
• A mechanism

## Slide 27: One more definition
Coherence defines the behavior of read and write to the same memory location
Consistency defines reads and writes with respect to accesses to other memory locations

## Slide 28
Cache coherency and consistency define the action of the processors to maintain coherence. More precisely, coherency defines what value is returned on a read, and consistency defines when it is available
Multiprocessor Consistency
• When does a memory write show up at another CPU?
• A programming model
Multiprocessor Coherence
• How are memory accesses coordinated among CPUs?
• A mechanism

## Slide 29: Approaches to Coherency
Write Invalidate (Invalidation based protocol)
When a processor writes into C, all copies of it in
other processors are invalidated.
Write Broadcast (Broadcast based protocol)
  Instead of invalidating, why not broadcast the updated
  value to the other processors sharing that copy?
  This will act as write through for shared data, and
  write back for private data.
Software based approach
Do not cache shared data or cache “read only” data

## Slide 30: Snooping
Every cache with a copy of data also has a copy of sharing status of block, but no centralized state is kept
All caches are accessible via some broadcast medium (a bus or switch)
All cache controllers monitor or snoop on the medium to determine whether or not they have a copy of a block that is requested on a bus or switch access

## Slide 31: MESI Protocol (Papamarcos & Patel 1984)
It is a version of the snooping cache protocol.
Each cache block can be in one of four states:
  MODIFIED Valid block, but copy in M-block is not valid
  EXCLUSIVE No other cache has this block, M-block is valid
  SHARED Multiple caches may hold valid copies.
  INVALID Not valid

## Slide 32: MESI…
EVENT | Local | Remote
Read Hit | Use Local copy | No Action
Read Miss | I to S, or I to E | (S,E,M) to S
Write Hit | (S,E) to M | (S,E,M) to I
Write Miss | I to M | (S,E,M) to I
When a cache block changes its status from M, it first updates
the main memory

## Slide 33: Examples of state transition under MESI…
A. Read Miss
X=5
X=5
X=5
X=5
X=5
X=5
X=5
X=5
X=5
X=5
X=4
X=4
X=2
X=2
X=3
S
S
S
S
S
S
I
I
I
E
I
I
X=5
X=5
X=5
X=5
X=3
S
S
S
I

## Slide 34: MESI…
X=9
X=3
X=4
X=4
X=2
X=2
X=9
X=9
X=5
X=9
X=9
X=9
X=4
X=2
X=3
M
I
I
I
I
I
S
B, More Read Miss
S
Write back Mem first
Try again

## Slide 35: MESI…
C. Write Miss
X=9
X=4
X=2
X=5
M
I
I
I
X=9
X=4
X=2
X=9
X=9
X=4
X=2
X=9
X=9
X=9
X=4
X=2
X=9
X=10
I
I
I
M
Write back
Mem
Allocate X
Now Modify

## Slide 36: Directory Based
Sharing status of a block of physical memory is kept in just one location, the directory

## Slide 37: What is Hyper threading?
Another name for it is Symmetric Multi Threading (SMT)
SMT uses fine-grain control already present inside
an OoO superscalar to allow instructions from
multiple threads to enter execution on same clock
cycle. Gives better utilization of machine resources.

## Slide 38: Let Us Compare

## Slide 39: Software is the key…
Intel, Cisco, AMD have announced plan to come out with 80 to 256 core within a year.
The question is, what do we do with that much computational power?
256 cores would be useless, if one can’t generate 256 threads to work with.
Media applications should surely benefit from multicore.
What other applications would be necessary?
Can you name the seven Dwarfs?
It is a pattern of computation and communication.

## Slide 40: They are
Phillip Collela suggested these seven original Dwarfs for high end computing
Structured Grid
Dense linear algebra
Sparse linear algebra
N-body problem
Spectral methods (e.g.FFT)
Unstructured Grid
Monte Carlo (Map reduce)

## Slide 41: Some specific ones to Embedded systems
Graph Traversal
Dynamic Programming
Graphical Methods
Finite State Machine

## Slide 42: So the Future is (Conclusion…)
Many Core systems with strong parallelization.
Development of parallel algorithms in the select areas.
Parallel programming is not too difficult ;-)

## Slide 43
Thank you