## Slide 1: Practice Question Cache
Cache related Issues

## Slide 2: Problem 1
Loop A | Loop B
sum = 0; for (i = 0; i < 128; i++) for (j = 0; j < 64; j++) sum += A[i][j]; | sum = 0; for (j = 0; j < 64; j++) for (i = 0; i < 128; i++) sum += A[i][j];
Consider following two loops written in C, which calculates the sum of the entries in a 128 by 64 matrix of 32 bit integer
The matrix is stored contiguously in memory in row-major order. Row major order means that elements in the same row of the matrix are adjacent in memory A[i][j] resides in memory location [4*(64*i + j)]

## Slide 3
Assume that the caches are initially empty. Also, assume that only accesses to matrix cause memory references and all other necessary variables are stored in registers. Instructions are in a separate instruction cache.
Consider a 4KB direct-mapped data cache with 8-word (32-byte) cache lines.
Calculate the number of cache misses that will occur when running Loop A.
Calculate the number of cache misses that will occur when running Loop B.

## Slide 4
In a direct mapped cache, each element of cache can only be mapped
in a particular location. This matrix has 64 columns and 128 rows. Since each row of matrix has 64, 32-bit integers and each cache line
can hold 8 words, each row of matrix can fit into (648) = 8 cache lines
Answer Part 1
0 | A[0][0] | A[0][1] | A[0][2] | A[0][3] | A[0][4] | A[0][5] | A[0][6] | A[0][7]
1 | A[0][8] | A[0][9] | A[0][10] | A[0][11] | A[0][12] | A[0][13] | A[0][14] | A[0][15]
2 | A[0][16] | A[0][17] | A[0][18] | A[0][19] | A[0][20] | A[0][21] | A[0][22] | A[0][23]
3 | A[0][24] | A[0][25] | A[0][26] | A[0][27] | A[0][28] | A[0][29] | A[0][30] | A[0][31]
4 | A[0][32] | A[0][33] | A[0][34] | A[0][35] | A[0][36] | A[0][37] | A[0][38] | A[0][39]
5 | A[0][40] | A[0][41] | A[0][42] | A[0][43] | A[0][44] | A[0][45] | A[0][46] | A[0][47]
6 | A[0][48] | A[0][49] | A[0][50] | A[0][51] | A[0][52] | A[0][53] | A[0][54] | A[0][55]
7 | A[0][56] | A[0][57] | A[0][58] | A[0][59] | A[0][60] | A[0][61] | A[0][62] | A[0][63]
8 | A[1][0] | A[1][1] | A[1][2] | A[1][3] | A[1][4] | A[1][5] | A[1][6] | A[1][7]
   |    |    |    |    |    |    |    |   

## Slide 5
A Loop A accesses memory sequentially (each iteration of Loop A sums a row in the matrix ), an access to a word that maps to the first word in a cache line will miss but the next seven accesses will hit.
Therefore, Loop A will only have compulsory misses (128648 or 1024 misses).

## Slide 6
Answer Part 2
Each iteration of Loop B sums a column in the given matrix. Hence
consecutive accesses in Loop B will use every eighth cache line.
Why?
A[0][0], A[1][0],A[2][0],…,A[126][0],A[127][0]
We store the matrix in a row-major order and each row takes up 8 cache line. Within this 8 cache line, only the first element is of interest to the Loop B as it wants to read a column.
Hence fitting one column of the given matrix, we would need
128 x 8 = 1024 cache lines

## Slide 7
0 | A[0][0] | A[0][1] | A[0][2] | A[0][3] | A[0][4] | A[0][5] | A[0][6] | A[0][7]
1 | A[0][8] | A[0][9] | A[0][1] | A[0][1] | A[0][1] | A[0][1] | A[0][14] | A[0][15]
2 | A[0][16] | A[0][17] | A[0][18] | A[0][19] | A[0][20] | A[0][21] | A[0][22] | A[0][23]
 | …. …. ….. …. ….. ….. ….. …… ….. ….. ….. ….. |  |  |  |  |  |  | 
7 | A[0][56] | A[0][57] | A[0][58] | A[0][59] | A[0][60] | A[0][61] | A[0][62] | A[0][63]
8 | A[1][0] | A[1][1] | A[1][2] | A[1][3] | A[1][4] | A[1][5] | A[1][6] | A[1][7]
9 | A[1][8] | A[1][9] | A[1][10] | A[1][11] | A[1][12] | A[1][13] | A[1][14] | A[1][15]
7 | …. …. ….. …. ….. ….. ….. …… ….. ….. ….. ….. …… ….. ….. |  |  |  |  |  |  | 
16 | A[2][0] | A[2][1] | A[2][2] | A[2][3] | A[2][4] | A[2][5] | A[2][6] | A[2][7]
 | …. …. ….. …. ….. ….. ….. …… ….. ….. ….. ….. …… ….. ….. |  |  |  |  |  |  | 
24 | A[3][0] | A[3][1] | A[3][2] | A[3][3] | A[3][4] | A[3][5] | A[3][6] | A[3][7]
 | …. …. ….. …. ….. ….. ….. …… ….. ….. ….. ….. …… ….. ….. |  |  |  |  |  |  | 

## Slide 8
In 4kB cache with 32B per cache line, there can be only 128 cache lines present at anytime.
So to get one complete column, we need 1024 cache lines but due to the capacity of cache, there can be only 128 cache lines present.
This means that while executing Loop B, each cache access will be a miss – either compulsory or conflict (as bringing in new cache lines will evict older cache lines)

## Slide 9
Additional Problem for extra credit
Calculate the minimum number of cache lines required for the data cache if Loop A is to run without any cache misses other than compulsory misses.
Answer: 1 cache line
Calculate the minimum number of cache lines required for the data cache if Loop B is to run without any cache misses other than compulsory misses.
Answer: 1024 cache lines

## Slide 10: ILP vs Reducing Cache misses
Sometimes a compiler has to choose between improving ILP and improving cache performance
Example:
for (i= 0; i < 512; i = i + 1)
for (j = 1; j < 512; j = j + 1)
x[i][j] = 2*x[i][j-1];
This code accesses the data in the order they are stored thus minimizing the cache misses, but if you unroll the loop, you will find that
for (i= 0; i < 512; i = i + 1)
for (j = 1; j < 512; j = j + 4) {
x[i][j] = 2*x[i][j-1];
x[i][j+1] = 2*x[i][j];
x[i][j+2] = 2*x[i][j+1];
x[i][j+3] = 2*x[i][j+2];
};
Here last three statements have RAW dependency…

## Slide 11
To improve the parallelism, two loops can be interchanged…
for (j = 1; j < 512; j = j + 1)
for (i= 0; i < 512; i = i + 1)
x[i][j] = 2*x[i][j-1];
Unrolling this loop would show
for (j = 1; j < 512; j = j + 1)
for (i= 0; i < 512; i = i + 4){
x[i][j] = 2*x[i][j-1];
x[i+1][j] = 2*x[i+1][j-1];
x[i+2][j] = 2*x[i+2][j-1];
x[i+3][j] = 2*x[i+3][j-1];
};
Now all four statements are independent and can be executed in parallel
But this would lead to memory accesses that would hop through memory thus reducing spatial locality and cache hit rate…